## Slide 1: LEF Comparison Tool
Matthew Miller
James Exterkamp
Joshua Ashley
EE 584

## Slide 2
LEF Comparison Tool
  LEF data is generated in a random order
    Makes diffs between LEF files practically useless
    Identical source files can generate very different LEF files
  LEF files can be sorted
    No effect on data stored
    Sorted LEF files can be diffed

## Slide 3: LEF Files
Library Exchange Format (LEF)
LEF files are files used to store the physical layout of an integrated circuit
  It is analogous to the layout view
  It only stores the
The file is organized into the following hierarchy
  Cell
    Cell Properties
    Pins
      Pin Properties
      Port
        Layers
          Coordinates of Layers
    Obstructions
      Layers
        Coordinates of Layer Obstructions

## Slide 4
Starting Point
First, a definition
  In this presentation, 'Tier' refers to any one Cell, Pin, Layer, or Obstruction.
Ruby script provided
  Sorts within each Layer in the LEF file
  Other tiers of data are left unsorted
Intended object-oriented structure
  Each Tier is described by a class.
  These classes all have the following functions defined:
    is_start_line
    initialize
    sort
    print
  Creating a new Tier calls initialize(file, index), which parses the file from the location noted in index until it recognizes an end delimiter. Attempting to initialize a Tier with a bad starting location raises an error.
  A call to sort() on a Tier will call sort() for all child Tiers, and then sort the properties of the original Tier.

## Slide 5: sortLEFdata.rb
AS IT STANDS:
Reads in LEF file
  Checks file for errors, prints to screen
Optionally Reads in LIB file
  Check for LIB errors
  Compare LEF file against LIB file
Prints results to console and file.

## Slide 6: sortLEFdata.rb
IMPROVEMENTS:
Read in TLEF file
  Compare LEF file against for matching layers.
Compare LEF vs LEF
  LEF files with identical, but differently sorted data should show no differences.
Refactor Top Level
  Code does much more than sort a LEF file as the name implies.
  User should be able to tell the script exactly what to do
    What comparisons should be done?
    Print diff report or new file?